# ATTACHMENTS - Deviation Matrix

| No | Equipment |  | Pipe deck to CW | CW to Drill floor | HTV | Setback/Rotary | Slips | Stabbing/guiding | Make/Break | Description of non conformances and compensating measures in addition to general requirements. M = manual operation, NA = Not Applicable, R = Remote Operation, Compensating Measures: |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Drill Bit | Req. | M | M | NA | M | NA | NA | M | Drill bits shall preferably be installed onshore, before arrival the rig, in order to reduce manual operations offshore. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 2 | DC | Req. | R | R | R1 | R1 | R1 | R | R | R1 Operation can be performed manually when the DC have a total length of less than 300 m (does not apply for modified Drill Collars). DC with recess for elevator and slips to be used during remote operation, otherwise a slips type elevator shall be used. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 3 | Lifting Sub for DC and BHA | Req. | NA | NA | M | NA | NA | M | R1 | R1 Manual operation when lift subs are installed on DC joint on Cat Walk. Lift sub length adjusted to the rigs equipment shall preferably be installed and prepared onshore. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 4 | JAR | Req. | R | R | R | R | M | R | R | Norwegian Oil and Gas/NSA members should influence suppliers to deliver JAR with recess for elevator. If this is not possible, the Jar shall, if possible, be delivered with lifting sub with length fitted to rig equipment. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 5 | Dog-collar | Req. | NA | NA | NA | NA | M1 | NA | NA | M1 Use of Manuel Dog-collar clamp shall be limited. Remote operated Dog-collar shall be used when longer lengths of the same dimensions are run. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 6 | X/O | Req. | M | M | M | M | M | M | R1 | R1 Every rig must ensure that proper length of X/O’s suitable for remote operation is being used. New XO’s shall have a design that makes it possible for remote operation during make/break. X/O adjusted to the equipment shall preferably be prepared and assembled onshore. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 7 | Stabilizers / Hole opener | Req. | M | M | M | M | M | M | R1 | R1 On new builds, upgrading or replacement of Iron Roughneck, a system that handles stabilizers / hole openers remotely shall preferably be chosen. Stabilizers shall be designed in a way that makes it possible to part/split them with the Iron Roughneck. Stabilizers with removable rings must be avoided. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 8 | DP, HWDP | Req. | R | R | R | R | R1 | R | R2 | R1 Manual operation is allowed if string weight is less then recommendation from the equipment supplier, R2 All types of pipe, DP - DC etc. which has been exposed for "over torque” and cannot be broken with remote operated equipment, can be broken manually, see Attachment 3. Thin walled pipes can be made up manually (TLC, thin walled tubes etc.) All standard operations shall be remote operated. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 9 | Non Magnetic DC | Req. | R1 | R | R2 | R2 | R2 | R | R | R1 Manuel operation is permitted where a magnet is still in use. On new builds, upgrading or replacement of pipe deck cranes, a system that handles non-magnetic pipes, shall be selected. R2 Operation can be performed manually when the DC have a total length of less than 300 m (does not apply for modified Drill Collars). DC with recess for elevator and slips to be used during remote operation, otherwise a slips type elevator shall be used. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 10 | DP < 3 ½” | Req. | R | R | M | R1 | R2 | R3 | R | R1 Manual operation is allowed if no inserts are available in the market for pipes <3 ½”. R2 Manual operation is allowed if string weight is less then recommendation from equipment supplier. R3 Manual stabbing/guiding/centring can only be accepted in special cases; if the remote operated equipment cannot be adjusted to the correct dimension. On new build, upgrading or replacement of remote operated equipment, solutions that make remote operations possible shall be selected. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 11 | Casing | Req. | R2 | R2 | R | R | R1 | R | R2 | R1 Manual equipment can be used when the weight of the string is less then the recommendation from the supplier of the remote operated equipment. R2 Manuel handling of casing > 20” The casing shall be filled from a suitable arrangement through the topdrive, such that work in red zone is avoided. Ref. attachment 3, deformed or impaired pipes. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 12 | Non Magnetic Casing | Req. | R1 | R | R | R | R2 | R | R | R1 Manual operation is permitted only where magnets still are being used. R2 Manual equipment can be used when the weight of the string is less then the recommendation from the supplier of the remote operated equipment. On new builds, upgrading or replacement of equipment, a system that makes remote operation possible shall be selected. Ref. attachment 3, deformed or impaired pipes. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 13 | Slick Casing / Liners | Req. | R | R | R1 | NA | R | R2 | R | R1 Applies only for make / break of lift subs, otherwise a manual slips type elevator shall be used. R2 Manual installation of Stabbing Guide can be accepted where it can lead to damage to seal area /threads. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 14 | Centralizers | Req. | NA | NA | NA | NA | NA | NA | R1 | R1 Centralizers shall preferably be installed onshore. Manual handling can be done if no other type of centralizer will work with the pipe handling equipment. On new builds, upgrading or replacement of equipment, a system that makes remote operation possible shall be selected. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 15 | WO Riser <20” | Req. | R | R | R | R | R | R | M | Short pipes and XO’s can be handled manually. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 16 | Marin Risers and Slip Joint > 20” | Req. | M | M | M | R | M | M | NA |  |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 17 | BOP Test Tool | Req. | M | M | NA | M | M | M | R |  |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 18 | Perforating Guns | Req. | R1 | R | R | NA | R | R | R | R1 Perforating guns shall not be handled with magnet cranes. Perforating guns built for remote operation shall be used, unless specific requirements to function is not available in the market. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 19 | Fishing Equipment | Req. | M | M | M | M | M | M | M | With reference to XO, current manual handling of fishing equipment can be accepted. This is not a standard operation. A Safe Job Analyses (SJA) shall be performed before releasing the fish on deck. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 20 | Protectors | Req. | NA | NA | R1 | NA | NA | NA | NA | R1 On new builds, upgrading or replacement of equipment; A system that enables remote operation of tubulars (without protectors), shall be selected. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 21 | Mud Bucket | Req. | NA | NA | NA | F | NA | NA | NA |  |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 22 | Dope | Req. | NA | NA | NA | R1 | NA | NA | NA | R1 On new builds, upgrading or replacement of equipment, a system that makes remote operation possible, shall be selected. Casing and tubing shall be doped onshore prior to shipping offshore. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 23 | DP Pup Joints | Req. | M | M | M | M | F | M | R | Every rig has to research and find the proper length for Pup Joints suitable for remote operation or Pup Joints must be replaced to fit rig equipment. This must be documented. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 24 | Casing/Tubing and Pup Joints | Req. | R | R | R | R | R1 | R | R | R1 Manual equipment can be used when the weight of the string is less then the recommendation from the supplier of the remote operated equipment. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 25 | Non magnetic Casing/Tubing and Pup Joints | Req. | R1 | R | R | R | R2 | R | R | R1 Assemblies that are too long for remote operated handling, can be handled manually. Manual operation is allowed where magnets are still in use. R2 Manual equipment can be used when the weight of the string is less then the recommendation from the supplier of the remote operated equipment. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 26 | Screens | Req. | M | R | R | R | R | M | M | Sensitive completion components which can be damaged of remote operated equipment can be operated manually. In that case, a HAZID shall be performed. SJA shall be performed before the operation starts. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 27 | Inner string | Req. | R | R | M | M | M | M | M | 2 7/8" and 3 1/2" string shall be standardized to fit remote operated rig equipment. If the joint cannot be racked in the derrick in a safe way, the joints must be laid down (remote operated). |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 28 | Lateral Well Equipment | Req. | M | M | M | M | M | M | M | Operations which can be remotely operated shall be remotely operated. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 29 | Completion Equipment | Req. | M | M | M | M | M | R1 | M | R1 For equipment which can be made up for remote operation, operation shall be remotely operated. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 30 | Double Production Tubing | Req. | M | R | M | R | R | M | M | Equipment and components which can be damaged by using remote operated equipment can be manually handled. A HAZID shall be prepared and a SJA executed prior to start of operation. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 31 | MWD / Mud Motors | Req. | R | R | R | R | M | M | M | Equipment and components which can be damaged by using remote operated equipment can be manually handled. Equipment should be fit for remote operation and lifting sub should be avoided. For lifting sub, see item #3. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 32 | Coil Tubing BHA’s | Req. | M | M | M | M | M | M | M | BHA’s shall if possible be prepared and made up onshore. Operations that can be remotely operated shall be remotely operated. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 33 | False Rotary Table | Req. | NA | NA | NA | R | R | R | R | Pipe that normally shall be remotely operated shall also be operated remotely by use of false rotary table. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 34 | Drilling with Pup Joint / Drilling Stand | Req. | NA | NA | NA | R | R | R | R1 | R1 If the iron roughneck is not designed to function as a “back up” tong, a manually rig tong can be used. Procedure(s) shall be worked out. On new builds, upgrading or replacement of equipment, a system that makes remote operation possible shall be selected. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |
| 35 | Casing/Liner Drilling | Req. | R | R | R | R | R1 | R | R | R1 If the weight of the string is less then recommended from the equipment supplier, manual operation is allowed. For retrievable BHA, manual operation is allowed. |
|  |  | Rig |  |  |  |  |  |  |  | Procedure no. |

## ATTACHMENT 2: Remote Operated Equipment Failures

Guideline for Temporary Failure of Remote Operated Pipe Handling Equipment.

## ATTACHMENT 3:  Pulling Deformed or Impaired Pipes

Guidelines while pulling Deformed or Impaired Pipes out of the hole.

## ATTACHMENT 4: Failure in anti-collision system

Guidelines for Temporary Failure of Anti-collision System, Crown Saver and Floor Saver.